## Slide 1
Applied Xeto | SkyPosium 2024
Leveraging new tech for the day-to-day toolkit
Michael Melillo, Solutions Architect | 10/17/2024

## Slide 2
End Goal & Some Intro Concepts
Before we get started…

## Slide 3
Sensor broadcasts data to Gateway
Gateway routes message from LAN through TTN Cloud
TTN MQTT Broker Application Publishes data to Subscribers
SkySpark MQTT Conn ingests MQTT Payload to configure records & ingest His Data
The End Goal

## Slide 4
Composite Specs
ph.points, ph.equips, etc.
Manufacturer device specs
Practitioner specs (fit for your implementation)
Composite specs are a mix and combination of different kinds of data ready-made for deployment in projects.

## Slide 5
xeto init acme.mylib
  Make sure your lib name is all lower case!
parseRef(“foo.lib::SpecName”).spec()
parseRef(“foo.lib”).specLib().specs()
spec.instantiate({graph}).map(row=> diff(null, row, {add}).commit())
From the git repo…
  xeto_findSpecByStringName
  xeto_findSpecByPropName
Some helper functions

## Slide 6
CSV Import
Now with xeto!

## Slide 7
Define Ideal Import Structure (csv format, `id, navName, specName, fooRef`)
Create a new spec lib (mm.csv)
Define new specs
Review new xeto_csvImport() function
xetoReload()
Run new import
CSV Workflow

## Slide 8
Traditional CSV Structure

## Slide 9
Spec Based CSV Structure
We could repeat the old structure
But why would we?

## Slide 10
CSV Import Demo

## Slide 11
Auto-Onboard Records
Leveraging obsMqtt to configure folio

## Slide 12
Review architecture
Inspect incoming MQTT payloads
Add new composite specs: Sensor-Points, Mqtt-His-Point, Elsys-Device
Review new xeto_mqttOnboard function
xetoReload()
Create obsMqtt task to consume MQTT traffic
MQTT Workflow

## Slide 13
MQTT Architecture
Sensor broadcasts data to Gateway
Gateway routes message from LAN through TTN Cloud
TTN MQTT Broker Application Publishes data to Subscribers
SkySpark MQTT Conn ingests MQTT Payload to configure records & ingest His Data

## Slide 14
Payload Format
obsPayload -> data -> uplink_message -> decoded_payload
These payload fields play a role in our spec definitions, not just our import func

## Slide 15
MQTT Demo Xeto Libs
mm.ttnmqtt
mm.pxeto
mm.elsys

## Slide 16
MQTT Demo

## Slide 17
Resources etc.
Source Code Repo: https://github.com/mikeMelillo/appliedXeto_skyposium2024
The Things Network
Elsys Sensors
LoRa Alliance
MQTT Protocol